## Slide 1: Lecture 11
Network Basics
Notes: <number>

## Slide 2: Network Definition
<number>
Set of technologies that connects computers
  Hardware, software & media
Allows users to
  communicate and collaborate
  Exchange information
  Share resources in real time

## Slide 3: The Uses of a Network
<number>
Simultaneous access to data
  Data files are shared
    Need to installing the programs on physical device is reduced.
    Provide new ways of communication like e-mail, IM.
  Shared files stored on a server
  Software can be shared
    Site licenses
    Network versions
    Application servers
Notes: <number>

## Slide 4: The Uses of a Network
<number>
Shared peripheral device
  Printers and faxes are common shares
  Reduces the cost per user
  Devices can be connected to the network
  Print servers control network printing
    Manage the print queue
Notes: <number>

## Slide 5: Sharing Data
<number>
File server contains documents used by other computers.

## Slide 6: The Uses of a Network
<number>
Personal communication
  Email
    Instantaneous communication
  Conferencing
    Tele conferencing
    Videoconferencing
    Audio-conferencing
    Data-conferencing
  Voice over IP
    Phone communication over network wires
Notes: <number>

## Slide 7: Voice Over IP
<number>

## Slide 8: The Uses of a Network
<number>
Easier data backup
  Backup copies data to removable media
  Server data backed up in one step
Notes: <number>

## Slide 9: Common Network Types
<number>
Local Area Network (LAN)
  Contains printers, servers and computers
  Systems are close to each other
  Contained in one office or building
  Organizations often have several LANS
Notes: <number>
Teaching tip
Use a real world example to describe an organization with interconnected LANs.

## Slide 10: Common Network Types
<number>
Wide Area Networks (WAN)
  Two or more LANs connected
  Over a large geographic area
  Typically use public or leased lines
    Phone lines
    Satellite
  The Internet is a WAN
Notes: <number>
Teaching tip
Blockbuster Video uses a WAN to connect it’s stores nationwide. Customers from Pittsburgh may rent videos in Hilton Head. Late fees will even be displayed!

## Slide 11: Hybrid Network Types
<number>
Campus Area Networks (CAN)
  A LAN in one large geographic area
  Resources related to the same organization
  Each department shares the LAN

## Slide 12: Hybrid Network Types
<number>
Metropolitan Area Network (MAN)
  Large network that connects different organizations
  Shares regional resources
  A network provider sells time
Notes: <number>
Teaching tip
An example of a regional resource is a supercomputer. For example, Pittsburgh has the Pittsburgh Super Computing center (www.psc.edu). The various colleges in Pittsburgh connect to the center through a MAN in Pittsburgh.

## Slide 13: Hybrid Network Types
<number>
Home Area Network (HAN)
  Small scale network
  Connects computers and entertainment appliances
  Found mainly in the home
Notes: <number>

## Slide 14: Hybrid Network Types
<number>
Personal Area Network (PAN)
  Very small scale network
  Range is less than 2 meters
  Cell phones, PDAs, MP3 players
Notes: <number>
Insider information
PAN is very new. Few devices support PAN. High end cell phones include Bluetooth technology. Once the technology matures, Bluetooth will allow the creation of a PAN.

## Slide 15: How Networks Are Structured
<number>
Server based network
  Node is any network device or a processing location
  Server-based networks include many nodes and one or more servers.
  The central computer is known as the file server or application server.
  Files and programs used by more than one user (at different nodes) are often stored on the server.
  Servers control what the node accesses
  Users gain access by logging in
  Server is the most important computer
Notes: <number>
Teaching tip
Spend a few minutes here discussing password policies. Describe why it is important not to give out a password. Also describe why longer, more complicated passwords are important.

## Slide 16: How Networks Are Structured
<number>
Client/Server network
  Nodes and servers share data roles
  Nodes are called clients
  Servers are used to control access
  Database software
    Access to data controlled by server
  Server is the most important computer

## Slide 17: How Networks Are Structured
<number>
Peer to peer networks (P2PN)
  All nodes are equal
  Nodes access resources on other nodes
  Each node controls its own resources
  Most modern OS allow P2PN
  Distributing computing is a form
Notes: <number>
Teaching tip
Discuss how users managing their own security settings can be bad.

## Slide 18: Network Topologies
<number>
Topology
  Logical layout of wires and equipment
  Choice affects
    Network performance
    Network size
    Network collision detection
  Several different types
Notes: <number>
Teaching tip
Discuss how your network topology handles collisions. If your students are technical, contrast this with an inferior topology.

## Slide 19: Network Topologies
<number>
Packets
  Pieces of data transmitted over a network
    Packets are created by sending node
    Data is reassembled by receiving node
  Packet header
    Sending and receiving address
  Packet payload
    Number and size of data
    Actual data
  Packet error control
Notes: <number>

## Slide 20: Network Topologies
<number>
Bus topology
  Also called linear bus
  One wire connects all nodes
  Terminator ends the wires
  Advantages
    Easy to setup
    Small amount of wire
  Disadvantages
    Slow
    Easy to crash
Notes: <number>
Teaching tip
Pages 352 and 353 have diagrams of each network topology

## Slide 21: Network Topologies
<number>
Star topology
  All nodes connect to a hub
    Packets sent to hub
    Hub sends packet to destination
  Advantages
    Easy to setup
    One cable can not crash network
  Disadvantages
    One hub crashing downs entire network
    Uses lots of cable
  Most common topology

## Slide 22: Star Topology
<number>

## Slide 23: Network Topologies
<number>
Ring topology
  Nodes connected in a circle
  Tokens used to transmit data
    Nodes must wait for token to send
  Advantages
    Time to send data is known
    No data collisions
  Disadvantages
    Slow
    Lots of cable

## Slide 24: Network Topologies
<number>
Mesh topology
  All computers connected together
  Internet is a mesh network
  Advantage
    Data will always be delivered
  Disadvantages
    Lots of cable
    Hard to setup

## Slide 25: Mesh Topology
<number>

## Slide 26: Network Media
<number>
Links that connect nodes
Choice impacts
  Speed
  Security
  Size

## Slide 27: Wire Based Media
<number>
Twisted-pair cabling
  Most common LAN cable
  Called Cat5 or 100BaseT
  Four pairs of copper cable twisted
  May be shielded from interference
  Speeds range from 1 Mbps to 1,000 Mbps
Notes: <number>
Insider information
Interference is usually electrical. Magnets, solar flares or electronic devices generate interference.

## Slide 28: Wire Based Media
<number>
Coaxial cable
  Similar to cable TV wire
  One wire runs through cable
  Shielded from interference
  Speeds up to 10 Mbps
  Nearly obsolete

## Slide 29: Wire Based Media
<number>
Fiber-optic cable
  Data is transmitted with light pulses
  Glass strand instead of cable
  Immune to interference
  Very secure
  Hard to work with
  Speeds up to 100 Gbps
Notes: <number>
Teaching tip
Remind students that bps is bits per second. Gbps then is billion bits per second.

## Slide 30: Wireless Media
<number>
Data transmitted through the air
LANs use radio waves
WANs use microwave signals
Easy to setup
Difficult to secure
Notes: <number>
Teaching tip
Now is the time to briefly discuss 802.11 standards. A full discussion of 802.11 is covered in the next section.

## Slide 31: Network Hardware
<number>
Network interface cards
  Network adapter
  Connects node to the media
  Unique Machine Access Code (MAC)
Notes: <number>
Insider Information
The Xerox Corporation controls the assignment of Ethernet addresses to NIC manufacturers.

## Slide 32: Network Hardware
<number>
Network linking devices
  Connect nodes in the network
  Cable runs from node to device
  Crossover cable connects two computers

## Slide 33: Network Hardware
<number>
Hubs
  Center of a star network
  All nodes receive transmitted packets
  Slow and insecure

## Slide 34: Network Hardware
<number>
Switches
  Replacement for hubs
  Only intended node receives transmission
  Fast and secure
Notes: <number>
Insider information
Twisted pair networks cannot achieve higher than 10 Mbps using a hub. Switches are necessary to achieve 100 Mbps or higher.

## Slide 35: Network Hardware
<number>
Bridge
  Connects two or more LANs together
  Packets sent to remote LAN cross
    Other packets do not cross
  Segments the network on MAC addresses

## Slide 36: Network Hardware
<number>
Router
  Connects two or more LANs together
  Packets sent to remote LAN cross
  Network is segmented by IP address
  Connect internal networks to the Internet
  Need configured before installation
Notes: <number>
Discussion point
Ask who in the class has high speed Internet. Then determine if anyone is sharing this to the rest of the house or dorm. If they are, see if they can describe the setup. Most likely, the sharing is done with a router.

## Slide 37: Network Hardware
<number>
Gateway
  Connects two dissimilar networks
  Connects coax to twisted pair
  Most gateways contained in other devices

## Slide 38: Network Cabling
<number>
Cabling specifications
  Bandwidth measures cable speed
    Typically measured in Mbps
  Maximum cable length
  Connector describes the type of plug

## Slide 39: Network Cabling
<number>
Ethernet
  Very popular cabling technology
  10 Base T, 10Base2, 10Base5
  Maximum bandwidth 10 Mbps
  Maximum distances100 to 500 meters

## Slide 40: Network Cabling
<number>
Fast Ethernet
  Newer version of Ethernet
  Bandwidth is 100 Mbps
  Uses Cat5 or greater cable
    Sometimes called 100Base T
  Requires a switch
Notes: <number>
Teaching tip
Point out that the speed of the cable is the number before the word Base.

## Slide 41: Network Cabling
<number>
Gigabit Ethernet
  High bandwidth version of Ethernet
  1 to 10 Gbps
  Cat 5 or fiber optic cable
  Video applications

## Slide 42: Network Cabling
<number>
Token ring
  Uses shielded twisted pair cabling
  Bandwidth between 10 and 25 Mbps
  Uses a multiple access unit (MAU)
  Popular in manufacturing and finance

## Slide 43: Network Protocols
<number>
Language of the network
  Rules of communication
  Error resolution
  Defines collision and collision recovery
  Size of packet
  Naming rules for computers

## Slide 44: Network Protocols
<number>
TCP/IP
  Transmission Control Protocol/Internet Protocol
  Most popular protocol
  Machines assigned a name of 4 numbers
    IP address
    209.8.166.179 is the White House’s web site
  Dynamic Host Configuration Protocol
    Simplifies assignment of IP addresses
  Required for Internet access
Notes: <number>
Teaching tip
Have students determine IP addresses for the computer. On 2000/XP enter ipconfig /all. Windows 98 and back enter winipcfg.

## Slide 45: Network Protocols
<number>
IPX/SPX
  Internet Packet Exchange/Sequenced Packet Exchange
  Older protocol
  Associated with Novell Netware
  Replaced by TCP/IP

## Slide 46: Network Protocols
<number>
NetBEUI
  Network BIOS Extended User Interface
  Used by Windows to name computers
  Transmission details handled by TCP/IP
Notes: <number>
Discussion Point
Have students tell you what BIOS stands for.

## Slide 47
End of Chapter
Copyright © 2006 by The McGraw-Hill Companies, Inc. All rights reserved.