## Slide 1: Lecture 6 Storage Technologies II
Md. Mahbubul Alam, PhD

## Slide 2: Objectives
1
Define the term average access time & its measurement
2
Explain the importance of file compression
3
Define the data transfer rate & its importance
4
Explain the way to optimize the computer’s performance
5
Identify drive interface standards used in PCs

## Slide 3: Drive Performance
An important factor in measuring overall system performance is the speed at which the computer’s disk drives operate.
Measures of drive performance generally are applied to the computer’s hard disk but also can be applied to other types of drives.
When evaluating the performance of common storage devices, two common factors needs to be considered:
        Average Access Time
        Data Transfer Rate

## Slide 4: Drive Performance: Average Access Time
  Also known as seek time
  The amount of time the device takes to move its read or read/write heads to any spot on the medium.
    Time to find desired data
  Average access time may vary depending on how far the heads need to move. It depends on two factors of the disk
        Revolutions per minute (RPM)  the speed at which a disk spins
        Time to access a track  the time it takes to move the heads from one track to another.
  Measurement of Average Access Time:
            Storage device: Milliseconds (ms)  one-thousands of a second.
            Memory device: nanoseconds (ns)  one-billionths of a second.
  Average Access Time:
    Hard drive: 6 to 12 ms
    CD-ROM drive: 80 to 800 ms

## Slide 5: Drive Performance (Data Transfer Rate)
  Other important factor of drive performance is speed at which it can transfer data.
      Speed the amount of time it takes for one device to send data to another device.
  Speeds are expressed as a rate  some amount of data per unit of time.
  In device’s data transfer rate (known as “throughput”) time is measured in seconds.
      Bytes per second (Bps) or bits per second (bps)
  Hard drive rate ranges from 15 to 160 MBps
  CD ROM rate depend on X factor
        24x CD transfers 24 x 150 KBps
  Floppy disks transfer rate at 45 KBps
Notes: Removable hard disks range from abou 1.25 MBps

## Slide 6: How to optimize disk performance?
Why?
  Over time, a PC’s performance can slow down.
  Drive performance may get slower in a older PC.
  New PC can suffer occasional performance downturns.
  A computer may act sluggish in general or slow down when performing specific task such as loading or saving documents.
How?
  Hard-disk maintenance or disk optimization.
  Use of operating system’s built-in tools or other utilities.

## Slide 7: Disk Optimization
Cleaning up Unneeded Files
  Remove temporary files (.tmp) & temporary Internet flies
  Remove/Uninstall Unneeded Programs
Scanning a disk for errors
  Scan the disk for errors, fix the errors, & possibly recover data that has been lost or corrupted because of a disk error.
  A disk error can a bad spot on the disk’s physical surface, or it can be a piece of data that cannot be accounted for in the FAT.
  Scanning a disk can be time-consuming process, but if the disk has errors, scanning may be able to fix problems and improve performance.
  Several versions of Windows have a built-in disk-scanning utility, otherwise you may buy very sophisticated disk scanners.

## Slide 8: Disk Optimization (cont’d)
Defragmenting a disk
  Fragmentation occurs when a file is stored in noncontiguous sectors on the disk’s surface.
  Pieces of files become scattered around the disk.
  During create, copy, delete files including install & uninstall programs over time, many files can become fragmented.
  Operating system keeps track of each fragment, however a greatly fragmented disk can slow system performance.
  It can take longer to find and load all the pieces of files as they needed by an application.
  How?
      Defragmentation utility
File Compression/data compression
  Related to the storage problems.
  Compress the data or files  shrinking the size of a file so it takes less space on the disk.
  This frees up space for more data and programs to reside on the disk.
  Compression files will not reduce a disk’s access time, however it can enable you to store more data on a disk, effectively increasing the disk’s capacity.
  Files can be compressed by as much as a 3:1 ratio (300 MB of data fill only 100 MB of space).
  File compression is performed by software that squeezes data into smaller chunks by removing information that is not vital to the file or data.
      e.g., PKZIP, WinZip, StuffIT, and DriveSpace (perform full disk compression).

## Slide 9: Disk Optimization (cont’d)
Drive-Interface Standards
  Another important factor in determining how quickly a drive can read and write data is type of controller that a drive uses.
  Just as video monitor requires a controller to act as an interface between the CPU and the display screen.
  Storage device also need a controller to act as an intermediary between the drive and the CPU.
  A disk controller
      Connects the disk drive to the computer’s bus
      Acting as an interface between the two
      Enables the drive to exchange data with other devices.
  Most personal computers use one of two drive-interface standards, either EIDE or SCSI
      Enhanced Integrated Drive Electronics (EIDE)
      Small Computer System Interface (SCSI)
      USB (Universal Serial Bus) and FireWire (IEEE 1394)

## Slide 10: End of Chapter